## Slide 1
SMART INDIA HACKATHON 2026
iTantra — Offline Voice Transceiver
Speech to text to speech, fully offline, over low-bitrate links.
Problem Statement ID – SIH26173
Problem Statement Title – iTantra - Indian Multilingual TTS & STT Aided Neural Transceiver Radio Access for low bitrate links
Theme – Smart Automation
PS Category – Software
Team ID – [PORTAL TEAM ID]
Team Name (Registered on portal) – B.J.P (Bug Janta Party)
PROPOSAL WITH LOCAL MEASUREMENTS • Integrated two-phone prototype and Android performance not yet validated

## Slide 2
IDEA TITLE
B.J.P (Bug Janta Party)
@SIH Idea submission- Template
2
iTantra | send voice as text, not as audio
Proposed Solution (Describe your Idea/Solution/Prototype)
An offline Android app: speech in, text out, tiny packet over Wi-Fi/Bluetooth, speech back out on the receiving phone.
Detailed explanation of the proposed solution
Push-to-talk works like a walkie-talkie. When idle, both phones run a full-duplex phone-style path. Alerts play at maximum volume and cannot be interrupted.
How it addresses the problem
Audio is too large for low-data-rate links. One spoken sentence becomes ~50-110 bytes of UTF-8 text — roughly 1,000x smaller — so voice fits where it could not before.
Innovation and uniqueness of the solution
Asymmetric pipeline: the speaker's phone carries the ASR cost, the listener's phone carries TTS. Idle listening runs only a voice-activity detector, so idle CPU stays near zero by design.

## Slide 3
TECHNICAL APPROACH
B.J.P (Bug Janta Party)
@SIH Idea submission- Template
3
Technologies to be used (e.g. programming languages, frameworks, hardware)
Kotlin Android app • sherpa-onnx (open-source, ONNX runtime) • Silero VAD (voice activity detection)
ASR: Meta Omnilingual CTC 300M INT8, Apache 2.0 • TTS: Piper VITS voices, MIT licence • Wi-Fi Direct / Bluetooth RFCOMM transport
Methodology and process for implementation (Flow Charts/Images/ working prototype)
PHONE A — SPEAKER
Mic 16 kHz mono
Silero VAD cuts sentence
Omnilingual ASR → text
Tag with language
TRANSPORT
Wi-Fi Direct (primary)
Bluetooth fallback
UTF-8 text only
~50–110 bytes per sentence
PHONE B — LISTENER
Piper TTS (hi / en)
Audio out 22050 Hz
Max volume, no interrupt
Alert loops until read
→
→
Measured on a development machine: ASR RTF 0.036–0.043, TTS RTF 0.032–0.044, full loop 0.29–0.42 s per utterance.
All figures measured on macOS arm64 (desktop), not on a phone. Android RTF and RAM remain unmeasured.

## Slide 4
FEASIBILITY AND VIABILITY
B.J.P (Bug Janta Party)
@SIH Idea submission- Template
4
Analysis of the feasibility of the idea
• Every component is open-source and permissively licensed (Apache 2.0 / MIT).
• ASR covers 1,668 languages; Hindi and English proven locally end to end.
• An official Android reference app already runs this exact ASR model with VAD.
Potential challenges and risks
• Phone CPU and RAM unmeasured; low/mid-range devices are the target.
• Clean-studio accuracy is not disaster-zone accuracy.
• Marathi measured weak (WER 0.74); 6 of 10 languages untested.
• Wi-Fi Direct behaves differently across Android vendors.
Strategies for overcoming these challenges
• Benchmark on the cheapest available phone first.
• Report CER alongside WER for complex scripts.
• Scope the demonstrator to Hindi + English, then extend.
• Ship Bluetooth fallback; never depend on one transport.
Planned proof: the two-phone walkie-talkie loop
Phone A speaks Hindi and English sentences; phone B must reproduce the same meaning as speech. Measure mouth-to-ear latency, idle CPU with VAD-only listening, peak RAM, and packet size on real devices.

## Slide 5
IMPACT AND BENEFITS
B.J.P (Bug Janta Party)
@SIH Idea submission- Template
5
Potential impact on the target audience
For field responders, volunteers and citizens on degraded or saturated networks: spoken alerts and instructions that reach the other end as intelligible speech, without requiring literacy or an internet connection.
Benefits of the solution (social, economic, environmental, etc.)
SOCIAL / proposed
Voice in, voice out — inclusive of users who cannot read or type. Alerts are heard, not read.
ECONOMIC / proposed
No paid API, no cloud, no proprietary SDK. Runs on phones people already own; only free open-source models.
ENVIRONMENTAL / proposed
Text instead of audio lowers transmitted energy per message; effect on battery runtime must still be measured.
Measured so far: Hindi and English round-trip cleanly with meaning intact; ~1,000x bandwidth reduction per sentence.
Not yet claimed: field accuracy in noise, phone-class latency, TTS legibility scores, battery runtime.
Benefits are proposed outcomes, not measured results. No claim of lives saved or guaranteed delivery at this stage.

## Slide 6
RESEARCH AND REFERENCES
B.J.P (Bug Janta Party)
@SIH Idea submission- Template
6
Details / Links of the reference and research work
Models and runtime
• csukuangfj/sherpa-onnx-omnilingual-asr-1600-languages-300M-ctc-int8-2025-11-12 — ASR, Apache 2.0, 348 MiB
• rhasspy/piper-voices hi_IN pratham and en_US lessac — TTS, MIT licence, ~60 MiB each
• k2-fsa/sherpa-onnx — Silero VAD (208 KB int8) and the SherpaOnnxVadAsr Android reference app
• Pre-built APK verified: sherpa-onnx-1.13.8-arm64-v8a-vad_asr-1600-omnilingual_asr_300M_ctc_int8.apk, 284 MiB
Evaluation data
• google/fleurs (CC-BY-4.0) — real recorded human speech used for per-language accuracy
Platform documentation
• k2-fsa.github.io/sherpa/onnx — VAD, ASR, TTS and Android guides
• developer.android.com — Wi-Fi Direct and Bluetooth P2P transport
Local evidence: end_to_end.py, tts_bench.py, fleurs_eval.py, convert_piper.py — all reproducible from this submission.